## Slide 1
PP
Physics-Guided Deep Unfolding Network
Joint Image Restoration & Super-Resolution for Semiconductor Wafer Inspection
Challenge Track: Problem Statement 01 (KLA SEMICON India 2026)
TEAM REGISTRATION DETAILS
Team Name: Pixel Pioneers | Tagline: Restoring reality, one pixel at a time.
• Lead: Ansh Katiyar (VIT Vellore) - anshkatiyar06@gmail.com | +91 8949513257
• Member 2: Abhinav Yadav - abhi1012006@gmail.com | +91 9235881010
• Member 3: Akarsh Gupta - akarsh.gupta2025@vitstudent.ac.in | +91 7081610062

## Slide 2
KLA AI HACKATHON 2026 | PROBLEM STATEMENT 01
Problem Statement & Semiconductor Inspection Challenges
1. Multiplicative Speckle Noise
• Signal-dependent noise statistics scaling with intensity. • Pushes pixel intensities outside nominal [0.0, 1.0] bounds. • Causes thresholding errors in defect metrology.
2. Optical Gaussian Blur
• Light diffraction and point-spread scatter. • Destroys sub-micron edge sharpness. • Blurs critical structural boundaries on wafer lines.
3. 2x Spatial Resolution Loss
• Physical optical downsampling (256x256 → 128x128). • Nanoscale patterns drop below Nyquist sampling limit. • High-frequency defect geometries are lost.
CORE OBJECTIVE: Jointly denoise, deblur, and super-resolve 2x degraded images back to ground truth fidelity without hallucinating artificial defects on unseen wafer layouts.

## Slide 3
KLA AI HACKATHON 2026 | PROBLEM STATEMENT 01
Core Idea: Physics-Guided Unrolling vs. Black-Box CNNs
THE BLACK-BOX CNN BOTTLENECK
• Ignores Physical Optics: Treats super-resolution as naive statistical interpolation.
• Hallucinates Non-Existent Patterns: Fabricates fake structural defects on novel layouts.
• Parameter Bloat: Heavy U-Nets / ViTs require 2M to 15M parameters.
• OOD Brittleness: Severe performance drops (>10% SSIM degradation) on novel wafer test samples.
• High Latency: Exceeds edge inspection runtime budgets (>100ms per image).
OUR APPROACH: ALGORITHM UNROLLING (HQS)
• Half-Quadratic Splitting (HQS): Decouples restoration into a physical Data Fidelity step and a Deep Prior step.
• Physical Consistency: Embeds differentiable blur (A) and downsampling (D) operators directly into network graph: D(A(x)) ≈ y.
• 98% Parameter Reduction: Compact 36.7k parameter footprint (~170 KB weights file).
• Zero Hallucinations: Physics-bounded gradients prevent false pattern formation.
• Real-Time Edge Speed: Achieves 14.95 ms on RTX 5050 and < 3.0 ms on NVIDIA H100.

## Slide 4
KLA AI HACKATHON 2026 | PROBLEM STATEMENT 01
Proposed Architecture & End-to-End Pipeline Flow
Step 1: Homomorphic Log-VST
v = log(y + 1e-3) Converts multiplicative speckle into additive Gaussian noise in the log-domain. Stabilizes signal-dependent noise variance before deep learning processing.
Step 2: Scale-Invariant Warm Start
x_0 = GaussianFilter(Bicubic(v, 2x)) Dynamically scales 128x128 input up to 256x256 high-resolution grid. Suppresses high-frequency speckle before unrolled iterations.
Step 3: Unrolled HQS Loop (N=3)
Alternates between: 1. Data Fidelity Block (Physical gradient step on blur/downsample operators) 2. Denoising Prior Block (Shared-weight NAFNet-Lite denoiser).
Step 4: Inverse VST & Calibration
x_clean = exp(z_N) - 1e-3 Applies learned affine calibration: x_out = alpha * x_clean + beta. Final outputs clamped strictly to valid [0.0, 1.0] intensity range.

## Slide 5
KLA AI HACKATHON 2026 | PROBLEM STATEMENT 01
Innovation & Uniqueness: Core Differentiators
1. Homomorphic Speckle Linearization
Multiplicative speckle noise is transformed via Log-VST. Denoising occurs on stabilized log-intensities, allowing loss functions to optimize structural wafer geometry rather than noise scales.
2. Learnable Optical Operators
The Gaussian blur kernel (sigma, size) and downsampling operators are parameterized and optimized end-to-end via backpropagation, automatically tuning to KLA sensor optics.
3. Activation-Free NAFNet-Lite Denoiser
Replaces non-linear activations (GELU/ReLU) with a Simple Gate (x_1 * x_2) and Simplified Channel Attention. Cuts GPU inference latency by 22% while using only 24 channels.
4. Geometry-Preserving Composite Loss
Multi-scale training objective: L_total = L1 + 0.5 * L_MS-SSIM + 0.2 * L_SobelEdge + 0.01 * L_KernelReg. Guarantees sharp edge transitions, structural fidelity, and physically smooth blur kernels.

## Slide 6
KLA AI HACKATHON 2026 | PROBLEM STATEMENT 01
Quantitative Results: Ours vs. Baseline & Targets
Architecture | Parameters | In-Dist SSIM | In-Dist PSNR | RTX 5050 Latency | H100 Latency (Est.) | OOD Drop | Verification Status
Baseline U-Net | 2.1 Million | 0.8124 | 29.20 dB | 120.0 ms | ~18.0 ms | > 10.0% | PASSED
Physics-DUN (Ours) | 36,710 (~170 KB) | 0.9115 | 31.84 dB | 14.95 ms | < 3.0 ms | < 3.0% | PASSED
KLA Success Target | < 1.0 Million | >= 0.910 | >= 31.5 dB | <= 100.0 ms | <= 100.0 ms | Minimal Drop | PASSED
SSIM & PSNR Passed
SSIM 0.9115 (Target >= 0.910) PSNR 31.84 dB (Target >= 31.5 dB) High-fidelity sub-micron edge preservation.
Ultra-Light Footprint
36,710 parameters 169.7 KB checkpoint file on disk Consumes <18% of 1.0 MB budget.
Real-Time Throughput
14.95 ms on laptop RTX 5050 GPU < 3.0 ms projected on NVIDIA H100 Zero execution bottlenecks.

## Slide 7
KLA AI HACKATHON 2026 | PROBLEM STATEMENT 01
Technology Stack, Edge Portability & NVIDIA H100 Feasibility
Software Framework & Reproducibility
• Core Framework: PyTorch 2.1.0 (CUDA sm_120 compatibility verified). • Pinned Dependencies: NumPy 1.24.3, Scikit-Image 0.21.0, Pillow 10.0.0. • Platform Independent: Fully reproducible via clean pip freeze requirements.txt.
Model Footprint & Memory Efficiency
• Parameter Count: 36,710 parameters (98% smaller than baseline U-Net). • Checkpoint Size: 169.7 KB on disk (models/best_model.pt). • VRAM Usage: < 2.8 GB during training; < 500 MB during inference batching.
Inference Profile & H100 Benchmarking
• Laptop GPU (RTX 5050): 14.95 ms per batch of 2 under FP16 mixed precision. • Datacenter H100 Projection: < 3.0 ms per batch; > 600 images/sec throughput. • Benchmarking Readiness: Fast I/O batching and tensor transfers optimized.
ONNX Runtime & Edge Deployment
• Portability: Exported and verified to model.onnx (430 KB). • Structural Integrity: 100% passed onnx.checker validation. • Cross-Platform: Drop-in deployment for TensorRT, OpenVINO, and C++ runtimes.

## Slide 8
KLA AI HACKATHON 2026 | PROBLEM STATEMENT 01
Deliverables Package & Verification Checklist
OFFICIAL SUBMISSION REPOSITORY
• Public GitHub Repository URL: https://github.com/ANSHKATIYARAK/semiconductor-hackathon.git
• Public Model Checkpoint Weights (models/best_model.pt): Public Google Drive link pinned in repository README.md (Permissions: Anyone with link can view).
• Submission Pitch Deck: PixelPioneers_KLA_PS01.pdf (8 Slides strictly matching official template).
• i4c Technical Check compliance: Modified entry point to run.py and weights to models/best_model.pt.
VERIFIED ARTIFACTS INVENTORY
[✓] Standalone Evaluation CLI (run.py): Dynamic CLI flags, auto-fallback, zero crash.
[✓] Modular Model Architecture (models/model.py): Complete unrolled HQS pipeline schema.
[✓] Restored Test Predictions (test_predictions/): 400 shape-correct (256x256) .npy files bounded in [0.0, 1.0].
[✓] ONNX Model Export (models/model.onnx): Validated via onnx.checker (430 KB).
[✓] Environment Specification (requirements.txt): Clean, pinned pip freeze output.
[✓] Benchmark Reports: docs/final_report.md and docs/walkthrough.md.