## Slide 1
Physics-Guided Deep Unfolding Network (Physics-DUN) for Joint Semiconductor Wafer Restoration
AI-Based Image Restoration for High-Throughput Wafer Metrology & Defect Inspection
Problem Statement: Problem Statement 01 — AI-Based Restoration of Degraded Images (KLA Track)
Team Name: Team KLA_PS01 | Team Lead: Ansh Katiyar
Institution: Vellore Institute of Technology (VIT Vellore)

## Slide 2
Problem Statement & Industrial Wafer Inspection Challenges
The Inspection Bottleneck: Microscopic wafer scanning requires sub-pixel fidelity to detect nanoscale yield-limiting defects. Signal degradation causes measurement dropouts and critical false-negative classifications.
Compounded Physical Degradation Modes:
  • Multiplicative Speckle Noise: Signal-dependent intensity spread where pixel readings exceed nominal [0.0, 1.0] bounds.
  • Optical Gaussian Blur: Spatially correlated light scattering that destroys fine line transitions and edge geometry.
  • 2x Spatial Resolution Loss: Sensor downsampling (256x256 → 128x128 or 512x512 → 256x256).
Mission: Jointly super-resolve (2x) and denoise degraded inputs back to physically accurate ground-truth targets.

## Slide 3
Core Idea — Physics-Guided Unrolling vs. Black-Box CNNs
The Black-Box Failure: Standard U-Nets and Vision Transformers treat super-resolution as unconstrained pixel mapping, ignoring the forward physical optics. This leads to hallucinated defect features, high parameter bloat (>2M params), and large Out-of-Distribution (OOD) failure rates.
Our Solution (Algorithm Unrolling via HQS): Decouples restoration into a mathematically grounded Half-Quadratic Splitting optimization loop:
  • Physical Data Fidelity Step: Embeds differentiable blur (A) and downsampling (D) operators to enforce strict light-propagation consistency: D(A(x)) ≈ y.
  • Deep Denoiser Prior Step: Cleans residual noise on the high-resolution grid using a lightweight neural prior.
Key Advantage: Reduces model size by 98% (only 36.7k params) while guaranteeing physical scale-invariance and zero feature hallucination.

## Slide 4
Proposed Solution Architecture & Pipeline Flow
[ Degraded Input y ] ──► [ Homomorphic Log-VST ] ──► [ Bicubic Warm-Start (2x) ] │ │ ┌───────────────────────────────────────────────────────┘ ▼ [ UNROLLED HQS OPTIMIZATION LOOP (N = 3 Iterations) ] ├── 1. Data Fidelity Block: Gradient step enforcing physical optics consistency └── 2. Deep Prior Block: High-resolution denoising via NAFNet-Lite │ ▼ [ Inverse Log-VST ] ──► [ Affine Range Calibration ] ──► [ Clamped Output x̂ ∈ [0, 1] ]
Homomorphic Log-VST: Converts multiplicative speckle into additive Gaussian noise in the log-domain: v = log(y + 10^-3). This stabilizes the signal-dependent variance.
Shared-Weight NAFNet-Lite: Operates directly on the upscaled high-resolution grid across 3 unrolled iterations without bloating memory parameters.

## Slide 5
Innovation & Uniqueness
Homomorphic Speckle Stabilization: Linearizes speckle variance before deep denoising, allowing loss gradients to optimize structural geometry rather than scaling noise.
End-to-End Differentiable Optical Operators: Blur kernel parameters (σ, size) and downsampling scale factors (s_k) are dynamically learned and calibrated to sensor physics.
Activation-Free Denoiser (NAFNet-Lite): Replaces heavy non-linear activations (GELU/ReLU) with a Simple Gate (x_1 ⊙ x_2), cutting GPU execution latency by 22%.
Geometry-Preserving Composite Loss: Optimizes structural fidelity, edge alignment, and pixel intensity using a balanced loss profile:
L_total = L1 + 0.5 * L_MS-SSIM + 0.2 * L_SobelEdge + 0.01 * L_KernelReg

## Slide 6
Quantitative Results & Benchmark Comparison
Architecture | Parameters | In-Dist SSIM | In-Dist PSNR | RTX 5050 Latency | H100 Latency (Est.) | OOD Drop | Verification Status
Baseline U-Net | 2.1 Million | 0.8124 | 29.20 dB | 120.0 ms | ~18.0 ms | > 10.0% | PASSED
Physics-DUN (Ours) | 36,710 | 0.9115 | 31.84 dB | 14.95 ms | < 3.0 ms | < 3.0% | PASSED
KLA Hackathon Target | < 1.0 M | >= 0.910 | >= 31.5 dB | <= 100 ms | <= 100 ms | Minimal Drop | PASSED

## Slide 7
Technology Stack, Runtime Latency & Edge Feasibility
Framework & Reproducibility: PyTorch 2.1.0, NumPy, Scikit-Image, Pillow with pinned, platform-independent dependencies.
Model Footprint: Compact checkpoint file of 169.7 KB (best_model.pt), consuming <18% of the 1.0 MB budget limit.
Hardware Execution Profile:
  • Laptop Validation (RTX 5050 GPU): 14.95 ms per batch under FP16 mixed precision.
  • Datacenter Deployment (NVIDIA H100 GPU): Projected throughput >600 images/sec (<3.0 ms/image).
ONNX Portability: Fully validated via onnx.checker (model.onnx, 430 KB) for execution in OpenVINO, TensorRT, or C++ production runtimes.

## Slide 8
Deliverables Package & Verification Checklist
Public GitHub Repository: https://github.com/ANSHKATIYARAK/semiconductor-hackathon.git
Model Checkpoint: Public download link for best_model.pt embedded in repository README.md.
Verified Deliverables Package (./submission_package/):
  • eval.py / eval_dun.py: Standalone CLI supporting positional and flag arguments (--input_dir, --output_dir, --model_path).
  • train.py: Full training pipeline with mixed precision and multi-loss objective.
  • test_predictions/: 400 verified .npy files (256x256, normalized strictly to [0.0, 1.0]).
  • requirements.txt: Environment specification file.