## Slide 1
Physics-Guided Deep Unfolding Network for Joint Semiconductor Wafer Inspection Image Restoration
KLA AI Hackathon - Problem Statement 1 Submission Team: Team KLA_PS01 | Lead: Ansh Katiyar

## Slide 2
Problem Statement & WAFER Inspection Challenges
Industrial Wafer Inspection: microscopic wafer scans require sub-pixel accuracy. Nanoscale defects are easily hidden by noise, causing yield-limiting measurement errors.
Compounded Physical Degradation: Images suffer from three simultaneous signal-degrading phenomena:
  1. Multiplicative Speckle Noise: Grainy noise scaling with local intensity, pushing degraded gray levels outside standard [0.0, 1.0] bounds.
  2. Gaussian Blur: Spatially correlated light scattering that destroys edge sharpness and geometric transitions.
  3. Spatial Resolution Loss: 2x optical sensor resolution constraints, downsampling outputs from 256x256 to 128x128 grid sizes.
Core Challenge: Super-resolve and denoise the 2x resolution degraded inputs back to clean, physical ground truth targets.

## Slide 3
Core Idea: Physics-Guided Unrolling vs. Black-Box CNNs
The Black-Box CNN Bottleneck: Standard restoration networks (e.g. U-Nets) treat super-resolution as a pure mapping task, ignoring optical degradation properties. They require millions of parameters, run slowly, and fail on Out-Of-Distribution (OOD) images.
Our Approach (Algorithm Unrolling): Decouples the restoration task into a mathematically formulated optimization loop (Half-Quadratic Splitting).
  1. Physical Fidelity Step: Explicitly embeds the forward degradation operators (blur, average pooling) to constrain outputs based on physical light propagation.
  2. Deep Denoiser Step: Uses a compact neural network (NAFNet-Lite) to eliminate remaining artifacts on the high-resolution grid.
Why it Wins: Guarantees physical scale-invariance, reduces model parameters by 98% (only 36.7k parameters), and ensures robust OOD generalization.

## Slide 4
Proposed Solution Architecture & Pipeline Flow
1. Homomorphic Preprocessing (Log-VST): Converts multiplicative speckle noise into additive Gaussian noise in the log-domain: v = log(y + 1e-3). This linearizes the noise statistics.
2. Scale-Invariant Warm Start: Bicubic upsamples the log-image by 2x and applies a mild Gaussian pre-filter to suppress high-frequency noise prior to unrolling.
3. Unrolled Optimization Loop (3 Iterations): Alternates between:
  Data Fidelity Block: A gradient descent step on the blur/downsampling matrix to enforce physical measurement matching.
  Denoising Prior Block: Clean spatial features on the HR grid using a shared-weight NAFNet-Lite model.
4. Post-processing & Range Calibration: Maps the log-estimate back via Inverse VST: x = exp(z) - 1e-3. Applies learned affine range calibration and clamps final values strictly to [0.0, 1.0].

## Slide 5
Innovation & Uniqueness Key Features
Speckle Stabilization: Log-VST homomorphic preprocessing linearizes speckle variance, allowing loss functions to optimize true geometry rather than scaling noise.
End-to-End Differentiable Physics: Blur operator parameters (kernel size, sigma) and downsample factors are learned dynamically during training, calibrating automatically to KLA sensor optics.
Activation-Free Denoiser (NAFNet-Lite): Replaces standard activations (GELU/ReLU) with a Simple Gate (multiplies split channel features), reducing GPU inference latency by 22%.
Geometry-Preserving Multi-Loss: Formulates the objective function as: L = L1 + 0.5 * MS-SSIM + 0.2 * Sobel Edge Loss + 0.01 * Kernel Regularization (enforces blur smoothness).

## Slide 6
Quantitative Results: Ours vs. Baseline U-Net
Model | Parameters | In-Dist SSIM | In-Dist PSNR | Latency | OOD SSIM Drop
Baseline U-Net | 2.1 Million | 0.8124 | 29.20 dB | 120.0 ms | > 10.0%
KLA-DUN (Ours) | 36,710 | 0.9115 | 31.84 dB | 14.95 ms | < 3.0%
Success Target | < 1.0 Million | >= 0.910 | >= 31.5 dB | <= 100.0 ms | Minimal Drop

## Slide 7
Technology Stack, Footprint & Runtime Latency
Software Frameworks: Built using PyTorch 2.1.0, NumPy 1.24.3, Scikit-Image 0.21.0, and Pillow 10.0.0. Minimal dependencies ensure high reproducibility.
Model Footprint: The trained checkpoint weighs only 169.7 KB on disk (best_model.pt), easily passing the sub-megabyte restriction.
Inference Latency Profile: Benchmarked on a consumer-grade laptop NVIDIA RTX 5050 GPU at 14.95 ms per batch. Projected to achieve < 3.0 ms latency on NVIDIA H100 datacenter clusters.
ONNX Portability: Successfully compiled and validated the network to 'model.onnx' (430 KB) using onnx.checker.check_model, supporting cross-platform integration inside OpenVINO, TensorRT, or CPU runtimes.

## Slide 8
Deliverables & Code Repository Access
GitHub Repository Link: https://github.com/ANSHKATIYARAK/semiconductor-hackathon.git
Model Checkpoint Download URL: Google Drive / Hugging Face weights download link is pinned in the repository README.md (Permissions: Anyone with link can view/download).
Deliverables Package Structure: Self-contained folder './submission_package/' contains:
  - best_model.pt: Trained parameter weights file (169.7 KB).
  - eval.py / eval_dun.py: Standalone evaluation CLI with positional and fallback parsing.
  - model.onnx: Ported ONNX model graph (430 KB).
  - requirements.txt: Pinned pip freeze environment requirements.
Status: Verified 400 predictions saved inside './test_predictions/' are shape-correct (256x256) and strictly bounded within [0.0, 1.0].